AMM-TE ammeter Manual

I. Kit Details

Kit Name: Ammeter Kit                           Kit Model: AMM-TE

PCB Size: 70.6 * 39mm                          Screen size: 51 * 24mm

Electrical parameters

Operating voltage: DC5V            Operating Current: 35mA      Accuracy: ± 1mA

Measurement range: 0 ~ 2A                 Outrange display: the first data 1 or -1

Display color: red

Ⅱ.Circuit Diagram

III. Circuit Principle

AMM-TE ammeter is mainly composed of ICL7107, the power supply circuit, a reference voltage source, the input circuit and display circuit.

1. ICL7107 is a BCD output of the integrator Type A / D converter chip, contains internal linear amplification, analog switches, vibration, display drivers and other components.

2. The power circuits into positive and negative supplies, the positive supply by the J2 input, C8 filter; negative power from the R8, Q1, L1, C6, C7, D2, D3 and ZD1 like, -5V voltage generated by the chip 26 feet input.

3. The reference voltage source is R1, R2, VR1, R9 and U2 constituted 36 feet for the reference voltage input pin, VR1 potentiometer to adjust the voltage of 100mV to 36 feet.

4. Enter the circuit J1, R5, R6 and C3 constitute, by measuring the current flowing through the circuit R5, it will produce a voltage on the R5, R6 after the voltage by limiting the input to the chip 31 feet for the treatment, C3 as input voltage filter capacitor.

5. The circuit consists of DS1 ~ DS4, D1, R3 configuration, four digital tube directly driven by the chip, R10 is DS1 ~ DS3 These three LED point limiting resistor.

IV. Finished debugging

1. Access DC 5V voltage (note polarity), or a digital display -.000 .000 is normal.

2. Use a multimeter to measure voltage chip 36 feet and 35 feet between the regulator VR1 potentiometer, so this is the pressure of 100mV can.

V. The key point voltage reference value

1. The chip 1 foot and 21 feet - voltage 5V

2. The chip 36 feet and 21 feet - voltage 100mV

3. The chip 26 feet and 21 feet - voltage -5V

Parts list

Note: Since the batch is not the same, could lead to some elements out of stock, it will be replaced with similar functions components

There are some differences between the products and the list! Use the material object as the standard!

| Name | Model/specification | Serial number | Quantity | Name | Model/specification | Serial number | Quantity |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 5-color resistance | 0.1R 2W | R5 | 1 | diode | 1N4148 | D1 D2 D3 | 3 |
|  | 2K | R1 R9 | 2 | voltage-regulatdiode | ST5V1 | ZD1 | 1 |
|  | 56K | R2 | 1 | Transistor | C1815 | Q1 | 1 |
|  | 1M | R6 | 1 | inductance | 2.2mH | L1 | 1 |
| 4-color resistance | 100R | R3 | 1 | Digital tube | 1bit common positive RED | DS1~DS4 | 4 |
|  | 270R | R10 | 1 | integrated circuit | ICL7107 | U1 | 1 |
|  | 20K | R8 | 1 |  | TL431A | U2 | 1 |
|  | 47K | R7 | 1 | Potentiometer | 3296 1K | VR1 | 1 |
|  | 100K | R4 | 1 | IC socket | 40P | U1 | 1 |
| Monolithic capacitors | 101P | C1 | 1 | terminal | 2P vertical type | J2 | 1 |
|  | 104P | C8 | 1 |  | 301-2P | J1 | 1 |
|  | 474P | C4 | 1 | power line | 2Psingle-end | 1 | 1 |
| CBB capacitance | 104P | C2 | 1 | PCB board | 70.6*39mm | 1 | 1 |
|  | 224P | C5 | 1 | light filter | 1 | 1 | 1 |
| Dacron capacitance | 103P | C3 | 1 | outer skin | 79*43mm | 1 | 1 |
| electrolytic capacitor | 10uF/25V | C6 C7 | 2 | screw | M1.7*6 | 4 | 4 |

Production steps

Before welding please carefully read the following steps, some of the installed components must be the order, this may lead to the production of unsuccessful!

- welding two colored ring resistance (color ring color is red dark brown brown, the same colors of the two resistance)

2. Welding a colored ring resistance (green blue black red brown)

- Welding a colored ring resistance (brown black black yellow and brown)

- Welding five four-color ring resistance

R3 color is brown black brown golden

R4 color is brown black yellow gold

R7 color is yellow purple orange gold

R8 color is red, black and orange gold

- Welding three diodes, three of the same model (with direction)

D1 D2 D3 model: 1N148

- welding a Zener diode (directional)

ZD1 model: ST5V1

7. welding a color ring inductance (color ring color is red red red silver)

- welding three monolithic capacitors

- Deal with the IC socket like this:

- Place the 1st row in the red box installation position (directional)

- Welding the 1st header row, install the four digital control (with directions)

- After welding finished four digital tube, cut off the excess pin digital

- Welding on the 2nd row home (with directions)

- Welding a transistor and a reference voltage regulator chips (with direction, and note to distinguish models)

Q1 model: C1815

U2 model: TL431A

- Welding 2 CBB capacitors and two electrolytic capacitors (electrolytic capacitors have direction)

- The welding a sampling resistor

- The welding a potentiometer and a polyester capacitor (potentiometer directional)

- welding power socket and input socket (both with directions)

- Install the IC, plug in the power cord (with direction), short circuit decimal point selection joints.

- Test Procedure:

1) Use DC 5V voltage (note polarity), digital display -.000 or .000 is normal

2) Adjust the VR1 potentiometer, so between 36 feet and 35 feet voltage is100mV

- Locking four screws, finished produced.